## Slide 1: ENGI 301 Dexter - Proposal
February 14, 2022
Prithve Kiran Shekar

## Slide 2: Background Information
I would like to create Dexter, a completely local voice assistant to integrate with my current Home Assistant setup
What I currently have:
A Dell thin client* running Debian (acting as a server), controlling my room’s lights and TV via Home Assistant (an open source, fully local home automation system). My goal was to prevent these devices from communicating with the cloud and collecting data on me. I’ve successfully accomplished that and can now control them completely locally, via Home Assistant’s interface. However, this requires me to navigate to its control panel, with my phone, laptop, or connect input devices to the server itself. It’s convenient enough on my phone, but it can be better.
What I would like to accomplish:
My primary goal is to control this system without needing to pull my phone out, or move away from what I may be working on with my laptop. I’d like to accomplish this in one of two ways – create a voice assistant to send specific commands to Home Assistant or create a physical dashboard on my desk to control my system. Either way, I’d like to use the PocketBeagle to send commands to my server to control my Home Assistant instance. My preference is to create the voice assistant (which I’m calling Dexter), but I’m open to creating the dashboard if processing power becomes a concern. Since I intend to send extremely specific commands however, I think this is a viable project.
* I will be able to bring it to class for a demonstration, the server itself fits in a backpack.

## Slide 3: Background Information
Intended Interaction flow
  Wake word recognition (via the Porcupine library) and acknowledgement via a sound response
    Alternative: Have a button to activate sound recording
  Record sound from microphone (using arecord) and store as a .wav file
  Local speech recognition from file (via Mozilla DeepSpeech)
  Parsing speech to recognize a command (via some sort of regex)
    Alternative: Use a dashboard comprising push buttons, switches, and potentiometers to generate a command
  Conveying command to Home Assistant (Over MQTT or somehow connecting to the server’s CLI)
    I’m not completely sure how to communicate with Home Assistant from the PocketBeagle, but it’s definitely possible, based on other voice assistants like Rhasspy (which I have had a terrible time trying to set up, ultimately motivating me to create my own)
Clearly the project uses lots of existing frameworks – the main advantages here being that the system will offload voice processing to a daughter board (the PocketBeagle), and the integration of these separate platforms to control Home Assistant. Alternatively, if the dashboard is created, it will give me a tactile and convenient way to interact with my system.

## Slide 4: System Block Diagram
5 Volts
OSD335x-SM SiP
Contains:
AM3358 TPS65217C TL5209 EEPROM
μUSB Host Connector
(To server)
5 Volts
USB0
USB1
Powered USB 2.0 Hub
(Amazon)
USB Speaker
(Sparkfun 18343)
USB Microphone
(Amazon)
5 Volts

## Slide 5: Power Block Diagram
5 Volts
OSD335x-SM SiP
Contains:
AM3358 TPS65217C TL5209 EEPROM
μUSB Host Connector
5 Volts
VIN_USB
SYS_VOUT
Powered USB 2.0 Hub
(Amazon)
USB Speaker
(Sparkfun 18343)
USB Microphone
(Amazon)
5V 0.8A
5 V 4A DC
AC Power
5V Up to 1.5A

## Slide 6: Components / Budget
Component | Need to Buy | Cost
PocketBeagle | No | -
USB A Female Connector for PocketBeagle (Sparkfun 12700) | Yes | 4.50
Powered USB Hub (Amazon) | Yes | 20.42
USB Speaker (Sparkfun 18343) | Yes | 9.85
USB Microphone (Amazon) | Yes | 28.99
Misc OEDK components (wires, buttons, etc) | No | -
TOTAL |  | 63.76
Need all components to be purchased by instructor listed; additional components may be purchased by student
Based on budget constraints I can definitely cut costs– this is what I’d ideally like to use though